## Slide 1: Employer Level Trenches & Excavations University of Cincinnati Department of Environmental and Public Health Sciences

## Slide 2: Disclaimer
This material was produced under grant number SH-05166-SH9 from the Occupational Safety and Health Administration, U.S. Department of Labor. It does not necessarily reflect the views or policies of the U.S. Department of Labor, nor does mention of trade names, commercial products, or organizations imply endorsement by the U.S. Government.
Notes: This is the required OSHA Susan Harwood grant disclaimer

## Slide 3: Introduction
In this course we will develop a thorough understanding of the 29 CFR 1926 Subpart P regulations and the responsibility employers have toward the safety of their employees.
Notes: The purpose is to ensure you have a solid understanding of the Subpart P regulations and employer’s responsibility for the safety of their employees.

## Slide 4: Learning Objectives
Identify worker rights and employer responsibilities under the OSH Act
Define 20+ key terms associated with the hazards and the safeguards of trenches and excavations
Discuss injury and illness statistics for trench and excavation work

## Slide 5: Learning Objectives
Recognize and accurately interpret common hazards associated with trenching and excavations
Identify root causes of hazard related incidents when working in and around trenches and excavations
Estimate the potential cost of injuries and citations associated with trenching and excavations
Define Subpart P Specific Excavation Requirements
Define Subpart P Requirements for Protective Systems

## Slide 6: Learning Objectives
Define Subpart P Appendices
Discuss effective elements of a trench and excavation safety program
Determine the necessary training required under Subpart P that workers need to identify and avoid hazards
Determine which individuals have the knowledge, experience, and qualifications to act as the competent person and discuss their duties as the competent person

## Slide 7: Let’s Test Our Knowledge
Pre-class Quiz

## Slide 8: Pre-Assessment (Q1)
Structural ramps used solely by employees as a means of access and egress from excavations shall be designed by a:
Qualified Engineer
Competent Person
Architect
Employees
Notes: The Answer is B

## Slide 9: Pre-Assessment (Q2)
2. Excavations must be inspected daily by an Authorized Person.
True
False
Notes: The Answer is B

## Slide 10: Pre-Assessment (Q3)
3. A “Trench Shield”, commonly known as a “Trench Box” in the field, is an engineered system designed to protect those who are working in a trench.
a. True
b. False
Notes: The Answer is A
This question may be confusing for students and the instructor should state that a “Trench Shield” is commonly known as, or commonly referred to as a “Trench Box” in the course.

## Slide 11: Pre-Assessment (Q4)
4. A Trench and an Excavation is the same thing:
True
False
Notes: The Answer is B

## Slide 12: Pre-Assessment (Q5)
5. Excavations greater than _____ ft. shall be tested before employees enter where potentially ______________ atmospheres could reasonably exist.
4’, Hazardous
4’, Ambient
6’, Hazardous
6’, Ambient
Notes: The Answer is A

## Slide 13: Pre-Assessment (Q6)
6. The bottom of a trench shield (trench box) should be no more than ______ ft. above the bottom of the trench or excavation?
5’
3’
1’
2’
Notes: The Answer is D

## Slide 14: Pre-Assessment (Q7)
7. ___________ cause/causes the most deaths in excavations.
Underground utilities
Water accumulation
Cave ins
Heavy equipment
Notes: The Answer is C

## Slide 15: Pre-Assessment (Q8)
8. In excavations deeper than 4’ a means of exit _________.
Is not needed
Must be located within 100’ of workers
Must be located within 200’ of workers
Must be located within 25’ of workers
Notes: The Answer is D

## Slide 16: Pre-Assessment (Q9)
9. Which of the following statements is not true about Type C soil:
If type is unknown, you should assume all soil is Type C
If sloped, it requires an angle of 34°
It can be benched
Type C soil is usually very loose and prone to cave in
Notes: The Answer is C

## Slide 17: Pre-Assessment (Q10)
10. ______________ involves angling back the material in a continuous plane.
Shoring
Shielding
Sloping
Benching
Notes: The Answer is C

## Slide 18: Worker Rights
  Workers have the right to:
  A Safe Workplace
  Certain employer provided information
  Make safety complaints
  Receive training
  Participate in OSHA inspections
Notes: Workers may request and receive information form the employer on OSHA’s rules and regulations, mandatory measuring or monitoring of toxic substances, and emergency procedures.
They can also make formal complaints in confidence to OSHA, receive OSHA mandated training, and participate in the “walk around” portion of an OSHA inspection.

## Slide 19: Worker Rights
  Workers have the right to:
  Refuse to perform dangerous work
  Examine OSHA records
  Hazardous chemical information
  Medical records
Notes: Workers may refuse to perform dangerous work if they reasonably believe there is a threat of serious injury or death and the employer refuses to correct the condition after the employee requests it.
They also have access to examine the OSHA 300 log of recordable injuries and illnesses, obtain safety data sheets for hazardous chemicals, and view work-related medical and exposure records.

## Slide 20: Worker Rights
  Workers have the right to:
  Contest the abatement period
  Participate in enforcement proceedings
  “Whistleblow” on employers
  Protection from discrimination
Notes: Workers have the right to contest an abatement period given to an employer by OSHA, intervene in enforcement proceedings against the employer, and report unsafe conditions or practices to OSHA without fear of retaliation from the employer.

## Slide 21: OSHA's FREE WORKPLACE POSTER
What is the OSHA poster and why do I need it?
The OSHA Job Safety and Health: It's the Law poster, available for free from OSHA, informs workers of their rights under the Occupational Safety and Health Act. All covered employers are required to display the poster in their workplace. Employers do not need to replace previous versions of the poster. Employers must display the poster in a conspicuous place where workers can see it.
If you are in a state with an OSHA-approved state plan, there may be a state version of the OSHA poster. Federal government agencies must use the Federal Agency Poster.
How do I get a copy?
You can get a copy of the OSHA poster in several ways:
Order a print copy online from the OSHA Publications webpage. The English version is publication number 3165. The Spanish version is publication number 3167.
Order a print copy by phone. Call OSHA's toll-free number at 1-800-321-6742 (OSHA) or the OSHA Publications Office at 202-693-1888.
Download a copy from the OSHA website. Note: OSHA requires that reproductions or facsimiles of the poster be at least 8.5" x 14" inches with 10 point type. Please see the instructions below for downloading a compliant version of the poster.
More Information Here: https://www.osha.gov/Publications/poster.html
Notes: 1903.2(a)(1)Each employer shall post and keep posted a notice or notices, to be furnished by the Occupational Safety and Health Administration, U.S. Department of Labor, informing employees of the protections and obligations provided for in the Act, and that for assistance and information, including copies of the Act and of specific safety and health standards, employees should contact the employer or the nearest office of the Department of Labor. Such notice or notices shall be posted by the employer in each establishment in a conspicuous place or places where notices to employees are customarily posted. Each employer shall take steps to insure that such notices are not altered, defaced, or covered by other material.

## Slide 22: Employer Responsibilities
  Employers are responsible to:
  Provide safe workplace
  Comply with OSHA
  Examine workplace conditions
  Warn of potential hazards
  Ensure safe tools & equipment
Notes: It is the employer’s responsibility to provide a workplace free of recognized hazards for its employees Complying with the Occupational Safety & Health Act and Administration, including all applicable regulations in 29 CFR 1904, 1910 and 1926, greatly help the employer do this. Other responsibilities they have include examining workplace conditions to determine their safety and warning employees of potential hazards with signs, etc. The employer also must ensure safe tools and equipment, whether they be provided by the employer or not.

## Slide 23: Employer Responsibilities
  Employers are responsible to:
  Have safe procedures
  Provide understandable safety training
  Have & train on hazcom
  Provide medical examinations when applicable
  Post employee rights poster
Notes: Having procedures explaining how to do work safely and providing training that can be understood by the employees receiving it fall under the employer’s responsibility. This may include having training in languages other than English if needed. Another responsibility of the employer is having a written hazard communication program if there are hazardous chemicals in the workplace. It is never acceptable to have employees work with chemicals without them receiving training on how to do it safely. Also, chemical safety information must always be available to employees and their representatives.
Employers are required to have certain medical examinations performed for employees under some OSHA regulations with cost going to the employer. Each employer must also post the employee rights poster (or state labor department equivalent) at each facility in a prominent location. The poster summarizes the rights of employees working in the United States.

## Slide 24: Employer Responsibilities
  Employers are responsible to:
  Report fatalities and serious injuries
  Keep records of injuries/illnesses
  Provide access to injury/illness log
  Provide access to medical/exposure records
  Not discriminate
Notes: There are several recordkeeping requirements for employers:
Reporting serious injuries (those involving amputations, loss of an eye, and hospitalizations of 3 or more) and fatalities to OSHA within 8 hours. States with state-run plans have their state’s OSHA office to report to while states under federal OSHA report to federal OSHA.
Keep records of injuries and illnesses on the OSHA 300 log and allow employee access to view logs. Logs are to be kept for 5 years.
Allow employee access to medical and exposure records related to work performed.
Employers are prohibited from discriminating against any employee for exercising their safety and health rights.

## Slide 25: Employer Responsibilities
  Employers are responsible to:
  Post citations
  Correct violations
  Adopt safety & health program
Notes: When employers receive citations, they are required to post them in or near the area of the violation in plain view for a prescribed number of days or until the hazard is abated. They are also given an abatement period, by the end of which they must prove to OSHA that the hazard has been abated.
Though not a requirement, OSHA highly recommends that all employer adopt and implement a safety and health program. It is anticipated that this will eventually become a requirement for employers under the OSH Act.

## Slide 26: Definition
Excavation:
  any man-made cut, cavity, trench, or depression in an earth surface, formed by earth removal

## Slide 27: Example
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-ND
Excavation-water in bottom
Notes: This is an excavation with water in the bottom.
Photo credit-creative commons.

## Slide 28: Definition
Trench (or trench excavation):
  a narrow excavation (in relation to its length) made below the surface of the ground
Notes: Trench-This definition is from OSHA. A trench is generally deeper than it is wide, but not more than 15 ft. wide at the bottom. A trench can also be made by having forms or other structures inside an excavation.

## Slide 29: Example
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Trench along road
Notes: This is a trench through and along a roadway.
Photo credit-creative commons.

## Slide 30: Definition
Cave-in:
  separation of a mass of soil or rock material from the side of an excavation….in sufficient quantity so that it could entrap, bury, or other wise injure and immobilize a person
Notes: Cave-in-The full OSHA definition includes “the loss of soil from under a trench shield or support system, and its sudden movement into the excavation, either by falling or sliding”

## Slide 31: Example
Cave-in at water utility excavation
This image courtesy of OSHA.
Notes: This is an excavation site after OSHA showed up and had workers evacuate. Their intervention prevented injuries and possibly deaths.
Photo credit-OSHA.
https://www.osha.gov/doc/trench-collapse.html

## Slide 32: Definition
Protective system:
  a method of protecting employees from cave-ins, from material that could fall or roll from an excavation face or into an excavation, or from the collapse of adjacent structures.
Notes: Protective system-This definition is from OSHA. OSHA also says that “Protective systems include support systems, sloping and benching systems, shield systems, and other systems that provide the necessary protection.”

## Slide 33: Protective Systems
Shoring
Shielding
Sloping
Notes: Left photo-an example of sloping the walls/faces of an excavation to eliminate the potential for cave-ins.
Photo used with permission from Benjamin Yaney.
Center photo-an example of shielding, using a trench box to protect the workers inside from the walls caving-in.
Shielding photo credit – David Ponder.
Right photo-an example of hydraulic shoring. Its purpose is bracing the walls of a trench excavation to support them, so they don’t cave-in.
Shoring photo credit – David Ponder.

## Slide 34: Image
This image courtesy of OSHA.
Notes: This image depicts sloping and shielding/shoring in an easy to remember fashion.
Image credit – OSHA.
https://www.osha.gov/SLTC/trenchingexcavation/

## Slide 35: Definition
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Sloping:
  method of protecting employees from cave-ins by excavating to form sides of an excavation that are inclined away from the excavation so as to prevent cave-ins.
Notes: Sloping-This definition is from OSHA. OSHA also says about sloping that “the angle of incline required to prevent a cave-in varies with differences in such factors as the soil type, environmental conditions of exposure, and application of surcharge loads.”
Photo credit-creative commons.

## Slide 36: Definition
This Photo by Unknown Author is licensed under CC BY
This image courtesy of creative commons.
Benching:
  method of protecting employees from cave-ins by excavating the sides of an excavation to form one or a series of horizontal levels or steps.
Notes: Benching-This definition is from OSHA. OSHA also includes “usually with vertical or near-vertical surfaces between levels.”
Photo credit-creative commons.

## Slide 37: Definition
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Support System:
  a structure such as underpinning, bracing, or shoring, which provides support to an adjacent structure, underground installation, or the sides of an excavation.
Notes: Support System-This definition is from OSHA.
Photo credit-creative commons.

## Slide 38: Definition
Shoring:
  a structure such as a metal hydraulic, mechanical or timber shoring system that supports the sides of an excavation and which is designed to prevent cave-ins.
Notes: Shoring-This definition is from OSHA. Shoring may also be called a shoring system.

## Slide 39: Definition
Shield:
  a structure that is able to withstand the forces imposed on it by a cave-in and thereby protect employees within the structure.
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Notes: Shield-This definition is from OSHA. OSHA also includes “shields can be permanent structures or can be designed to be portable and moved along as work progresses. Additionally, shields can be either premanufactured or job-built in accordance with 1926.652(c)(3) or (c)(4). Shields used in trenches are usually referred to as "trench boxes" or "trench shields."”
Photo credit-creative commons.

## Slide 40: Definition
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Cross brace:
  the horizontal members of a shoring system installed perpendicular to the sides of the excavation, the ends of which bear against either uprights or wales.
Notes: Cross brace-This definition is from OSHA.
Photo credit-creative commons.

## Slide 41: Definition
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Upright:
  the vertical members of a trench shoring system placed in contact with the earth and usually positioned so that individual members do not contact each other.
Notes: Upright-This definition is from OSHA. Uprights placed so that individual members are closely spaced, in contact with or interconnected to each other, are often called "sheeting."
Photo credit-creative commons.

## Slide 42: Definition
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Wales:
  horizontal members of a shoring system placed parallel to the excavation face whose sides bear against the vertical members of the shoring system or earth.
Notes: Wales-This definition is from OSHA.
Photo credit-creative commons.

## Slide 43: Definition
Kickout:
  the accidental release or failure of a cross brace.
Notes: Kickout-This definition is from OSHA.

## Slide 44: Definition
Failure:
  the breakage, displacement, or permanent deformation of a structural member or connection so as to reduce its structural integrity and its supportive capabilities.
Notes: Failure-This definition is from OSHA.

## Slide 45: Definition
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Face:
  the vertical or inclined earth surfaces formed as a result of excavation work.
Notes: Face-This definition is from OSHA. Also known as “side.”
Photo credit-creative commons.

## Slide 46: Definition
Accepted Engineering Practices:
  requirements which are compatible with standards of practice required by a registered professional engineer.
Notes: Accepted engineering practices-this definition is from OSHA.

## Slide 47: Definition
Bell-bottom Pier Hole:
  a type of shaft or footing excavation, the bottom of which is made larger than the cross section above to form a belled shape.
Notes: Bell-bottom pier hole-this definition is from OSHA.

## Slide 48: Definition
Structural Ramp:
  a ramp built of steel or wood, usually used for vehicle access.
Notes: Structural ramp-This definition is from OSHA. OSHA also says, “ramps made of soil or rock are not considered structural ramps.”

## Slide 49: Definition
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Ramp:
  an inclined walking or working surface that is used to gain access to one point from another, and is constructed from earth or from structural materials such as steel or wood.
Notes: Ramp-this definition is from OSHA.
Photo credit-creative commons.

## Slide 50: Definition
Tabulated Data:
  tables and charts approved by a registered professional engineer and used to design and construct a protective system.
Notes: Tabulated data-this definition is from OSHA.

## Slide 51: Statistics & Data
Two workers killed after trench collapses in Windsor
Video Courtesy of 9News Denver
Review YouTube clip
Trenching Fatalities Between 2013-2017
  Industrial construction sites (45)
  Private residences (39)
  Street and highway construction sites (28)
Notes: This data from the Bureau of Labor Statistics shows the number of fatalities in construction trenching and excavation work from 2013 to 2017, a five-year period. It is not an insignificant number-in 2016 there was a death an average of every other week. Many OSHA education and training groups focus on falls and excavation and trenching safety as they assist employers.

## Slide 52: Statistics & Data
Avulsion
Concussion
Crushing Injury
Cut, laceration
Joint Dislocation
Fracture
Internal injuries
Intracranial
Puncture
Soreness
Pain
Traumatic
Non-fatal Injury Types:
Notes: This list from OSHA’s online severe injury reports specifies 12 different types of injuries reported from trench and excavation work in 81 serious injuries since 2015. The most commonly occurring are fractures, then soreness, traumatic, internal and concussion injuries.

## Slide 53: Statistics & Data
Cave-in
Fall through surface
Fall to lower level
Fall from collapsing structure
Fall on same level
Slipping
Jump over or to a location
Non-fatal Injury Events:
Notes: This list from OSHA’s online severe injury reports show 7 different types of events that led to 81 serious injuries since 2015. All events have to do with walking/working surfaces or cave-ins. A fall into a trench that is 6 ft. or deeper is also a fall to lower level injury. It is safe to assume that some falls from heights or onto lower levels and some falls into excavations are placed into only one of the categories, thus showing less occurrence in records than.
Looking at the numbers, from 2015-2017 there averaged a little over 20 fatalities while there averaged a little under 20 serious injuries per year. What that tells us is that cave-in and falling hazards should always be corrected because over half the serious injuries are likely to result in death.

## Slide 54: Statistics & Data
This data courtesy of OSHA (cited by Federal OSHA during the period October 2018 through September 2019. Penalties shown reflect current rather than initial amounts.)
Standard | # of Citations | Penalty Amount
1926.651 Specific Excavation Requirements | 795 | $3.4M
1926.652 Requirements of Protective Systems | 613 | $4.2M
Citations & costs:
Notes: This table shows the direct cost to employers for not following regulations in 1926.651 and 652-over $7.5M! This is but one aspect of cost when it comes to unsafe trench and excavation work. Other costs include:
Medical costs for injuries
Additional labor and training after an injury
Lost productivity, morale
Increased overhead
Insurance costs
Lost earnings

## Slide 55: Direct Costs of Workplace Injuries
  At the surface
  Medical treatment
  Hospital bills
  Ambulance fees
  Indemnity (compensation to injured
Notes: Cover the direct cost of workplace injuries with the class

## Slide 56: Indirect Costs of Workplace Injuries
Below the surface
Damaged equipment
Legal fees
Accident Investigation
Schedule delays
Poorer customer relations
Lower worker moral; especially if a fatality occurs
Notes: Cover the indirect cost of workplace injuries with the class

## Slide 57: Practice: Scenario
During a safety inspection, you notice that a trench 6’ deep trench is not guarded by shielding, sloping (and benching) or shoring
Determine the costs:
  Estimate direct and indirect costs for the most likely resulting injury/illness (non-fatal cave in) if corrective actions are not taken
  Briefly list what factors you considered in arriving at your estimate in each area

## Slide 58: Practice: Determine Total Cost
Total = $84,090
Direct Cost $40,043 X 1.1 = $44,047 Indirect Cost
Direct Cost | Cost Multiplier
$0 - $2,999 | 4.5
$3,000 - $4,999 | 1.6
$5,000 - $9,999 | 1.2
$10,000 or more | 1.1
To calculate Indirect Cost, multiply direct cost by a cost multiplier.
The cost multiplier that you use will depend on the size of the direct cost.
To calculate Direct Cost of the Most likely injury: Cave in (broken leg)
Total value of the insurance claim for injury or illness $40,043

## Slide 59: Begin with Total Cost
A benefit to implementing corrective actions is the Return on Investment (ROI)

## Slide 60: Next, Total Investment
Incident to Prevent is Non-Fatal cave in (broken leg)
The corrective action selected is to install a trench shield
Calculate the total investment cost (add corrective actions and system improvements)
Total direct/indirect cost: $84,090
Total investment (rent a 6’tall trench shield): $1,500

## Slide 61: Practice
$82,590
$ 1,500
=55.06
5506%
Cost divided by Total Investment
Return on Investment
$84,090
1,500
$82,590
Total Cost minus Total Investment
Cost

## Slide 62: Hazard, Cause, Remedy
This image courtesy of MN Department of Public Safety
This image courtesy of OSHA.
Underground Utilities
Notes: Name some hazards associated with underground utilities and trenching (can be from photo or otherwise).
Photo-trench work with multiple utilities.
Left photo credit – OSHA.
https://www.osha.gov/SLTC/etools/hurricane/trenches.html
Right image credit-MN DPS
https://dps.mn.gov/divisions/ops/Pages/gopher-state-one-call.aspx

## Slide 63: Hazard, Cause, Remedy
No sidewall protection
No access/egress
Spoils are too close to the trenches edge

## Slide 64: Hazard, Cause, Remedy
Hazards | Causes | Remedies
Release of energy, weaken faces of excavation | Damage to or contact with utility | Avoid area, locate, purge or disconnect utility support or protect utility
Underground Utilities
Notes: Underground utilities-release of energy is the primary hazard with underground utilities.
Damaging or contacting underground utilities is a major cause of injury.
Avoiding the area is the easiest way to protect from those hazards. The next best thing is releasing stored energy in them before locating and carefully digging until they are reached. Once they are out, protecting them from contact damage or from lack of support are key. Additional details on hazards are below.
Natural gas-explosive, flammable, displaces oxygen
Sewer-toxic
Water-weakens excavation walls, is a drowning hazard, can impede egressing the trench
Electric-electrocution
Communication-electrocution
Stormwater-can hamper erosion control, is a drowning hazard, and may carry chemicals

## Slide 65: Hazard, Cause, Remedy
This image courtesy of MNOSHA.
Access & Egress
Notes: Name some hazards associated with access and egress (can be from photo or otherwise).
Left photo credit-creative commons.
Right photo credit – MNOSHA
https://dli.mn.gov/sites/default/files/pdf/construc_sem_excavation_trenching_0317.pdf

## Slide 66: Hazard, Cause, Remedy
No sidewall protection
Ladder not used as intended

## Slide 67: Hazard, Cause, Remedy
Hazards | Causes | Remedies
Unable to evacuate, slip, trip, fall, collapse, contact with equipment | Nonexistent or poor means or setup | Ensure adequate quantity and integrity of equipment, separate vehicles and personnel
Access & Egress
Notes: Access & egress-not having a safe way into or out of an excavation is a hazard. If workers need to evacuate an excavation, their exit cannot be too far away because it would take too long for them to get out. Workers cannot be expected to climb out of a trench using the walls, utilities or other equipment-they could easily trip, slip or fall and get injured. If the means of entrance or exit is not designed correctly and collapses, workers could get crushed or pinned by soil or equipment.
Primary causes of these hazards are not setting up access and egress properly (according to the regulations) or not having it at all. Sometimes, the setup is correct, but workers do not use it, which makes the cause system-related. Maybe the workers are not expected or instructed to use it.
Remedies to these hazards include having the right number and locations of entrances/exits and separating vehicles and equipment from pedestrians.

## Slide 68: Hazard, Cause, Remedy
This image courtesy of OSHA.
Vehicle & Equipment
Notes: Name some hazards associated with vehicles & equipment (can be from photo or otherwise).
Left photo used with permission from Benjamin Yaney.
Right photo credit – OSHA
https://www.osha.gov/SLTC/etools/construction/trenching/mainpage.html

## Slide 69: Hazard, Cause, Remedy
No sidewall protection
Ladder not used as intended (looks like an extension ladder taken apart)
Spoils are too close to the trenches edge

## Slide 70: Hazard, Cause, Remedy
Hazards | Causes | Remedies
Vehicle entry, struck-by load or equipment | Insufficient warning & barriers, personnel within working area of equipment | Designate and mark vehicle routes, establish restricted access zones for pedestrians
Vehicle & Equipment
Notes: Equipment & vehicular traffic-vehicles around trenches and excavations are also hazards. This may include traffic as well as equipment on the job site. Any vehicle accidentally entering a trench or excavation is bad for the driver and anyone working in the area. Soil, rocks or other debris that is removed from the excavation can fall and cause injuries to workers nearby. Many times, it can be difficult for equipment operators to be aware of who is in their work area because they are focused on what they are working on, so struck by digging, loading or unloading operations exist.
Causes include lack of warning equipment and barriers. Warning equipment may include traffic rerouting and directing as well as back up alarms and lights on equipment. Barriers are to prevent traffic vehicle entry as well as unintended equipment entry when visibility is limited. Another cause for these hazards is having personnel and equipment in the same working areas. Excavations are often limited in size and it is generally unsafe to have people on foot in the same zone as operated equipment.
Remedies include having an internal and external vehicle traffic control plan and executing it. It should include ensuring that all equipment has adequate warning devices and that the site does too. Most importantly, the worker will understand the process and expectations and can follow the procedure(s).

## Slide 71: Definition
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Hazardous atmosphere:
  an atmosphere which by reason of being explosive, flammable, poisonous, corrosive, oxidizing, irritating, oxygen deficient, toxic, or otherwise harmful, may cause death, illness, or injury

## Slide 72: Hazard, Cause, Remedy
This image courtesy of CPWR.
Hazardous Atmosphere
Notes: Name some hazards associated with hazardous atmospheres.
Left photo used with permission from Benjamin Yaney.
Right photo credit – CPWR
https://www.youtube.com/watch?v=iFahlN0ueTI

## Slide 73: Hazard, Cause, Remedy
Hazards | Causes | Remedies
Lack of oxygen, flammable or toxic air, inability to rescue | Untested or monitored atmosphere, fumes introduced, insufficient training, equipment | Have detailed rescue plan, test initially and during work
Hazardous Atmosphere
Notes: Hazardous atmosphere-vapors, dust or fumes in the air can displace oxygen, be toxic to breathe or may ignite and burn or explode. Knowing what might be in the atmosphere will help workers know what hazards might exist. If hazardous atmospheres are present, a lack of rescue plan or equipment is a hazard as well. Untrained or unprepared rescuers entering an excavation might get injured or stuck themselves, increasing the need for more rescuers.
Causes for these hazards include the failure to test or monitor an atmosphere, introducing fumes or hazards where there were none, and lack of rescue training or equipment.
Safe work can happen when a detailed rescue plan is in place and followed. It should include who is responsible for what as well as what equipment is needed and ensuring the equipment is in working order. In any excavation involving utilities or confined spaces, the best practice is to test the atmosphere for hazards initially and then monitor it throughout the job.

## Slide 74: Hazard, Cause, Remedy
Water Accumulation
Notes: Name some hazards associated with water accumulation (can be from photos or otherwise).
Right photo used with permission from Benjamin Yaney.
Left photo credit – OSHA
https://www.osha.gov/doc/trench-collapse.html

## Slide 75: Hazards Identified within the Photo
Water pooled inside the trench
Distance from the excavation wall to the trench box is greater
than expected surcharge.
Training, competent person and inspection seem to be missing
No access or egress
Trench height greater than 18” from top of box
Permit Required Confined Space
Unprotected hole
Improper slope

## Slide 76: Hazard, Cause, Remedy
Hazards | Causes | Remedies
Saturated soil cave-in, slips, drowning, electrocution | No shielding, failure to remove water, operating powered equipment in water | Pump out water, wait until dried out, protect powered equipment
Water Accumulation
Notes: Water accumulation-excavations with accumulated or accumulating water or that are saturated are hazardous for workers. If the water is deep enough, workers could drown if they fall, get stuck or can’t swim. Wet work areas always have slip hazards, and especially in trenches and excavations due to the uneven ground and likelihood of slick surfaces.
Water in an excavation may cause electrical tools and equipment to short out or not be sufficiently grounded, which are risks to workers. Saturated soil can impede workers from exiting an excavation. It also has less supportive strength and can cause walls or other features to fail.
Some causes of water accumulation hazards include not removing water or having workers work in saturated excavations without protection. Saturated soil loses stability and structure and weighs significantly more than dry soil, so it should not be taken lightly. Shielding is generally the best protective system when water is an issue. Another cause is operating electric equipment in or near water.
Powered equipment must be separated or protected from water when in use, and water can typically be pumped out or work can wait until water dries out.

## Slide 77: Hazard, Cause, Remedy
This image courtesy of CPWR.
Falling
Notes: Name some hazards associated with trench and excavation falling.
Right photo used with permission from Benjamin Yaney.
Left photo credit – CPWR
https://www.cpwr.com/sites/default/files/publications/TT-Trenches.pdf

## Slide 78: Hazard, Cause, Remedy
Hazards | Causes | Remedies
Rocks or soil falling into hole, nearby structures collapsing, walls caving-in | Spoils too close, insufficient support systems, incorrect soil type assessment | Distance spoils, support or remove structures, assume worst soil & protect from it
Falling
Notes: Stability-there are inherent stability hazards in every excavation just due to the nature of digging in the ground. Loose soil or rocks along the edges of excavations can fall and injure workers below. Surface encumbrances are any nearby structures that can become unstable due to the excavation-this can include trees, sidewalks, utility poles, or buildings for example. If any of those were to fall, slide, break or move unintentionally then workers nearby could get hurt. Cave-ins are generally the most serious hazard associated with excavations and trenches.
Causes of falling hazards include placing spoils too close to the excavation, not installing any or enough support systems on existing structures and improper soil classification or reclassification.
Placing spoils at least 2 feet from the excavation reduces the chance that loose soil or rocks will fall in. Supporting existing structures may include foundations or nearby buildings, sidewalks, or other equipment. Caution must be exercised here. If possible, support should be added before removing soil below the structures and as soil is removed. As far as soil collapsing, if you assume the worst type of soil (type C) and protect from that according to the standards, there should be no issue.

## Slide 79: Hazard, Cause, Remedy
Hazards | Causes | Remedies
Operator mistake (drops load, hits something), not knowing or following safe procedure | No competent person on site, untrained, poor safety program, lack of safe expectations | Train all workers, perform JSA, go over and use program, have consequences for unsafe behavior
Behavior
Notes: Workers, even with good intentions can make bad decisions themselves or have bad habits or attitudes that are hazardous. These may include poor operation of equipment, exhibiting overconfidence in ability or feeling like hazards or exposure doesn’t apply to them, being resistant to change from they way they have always done things, or just not knowing how serious a hazard is and thus ignoring it.
A lack of a safety program, competent person, safe work expectations or training could all contribute to poor behavior or decision making by workers.
Developing and using a trenching and excavation program can remedy behavior or decision-making issues. Workers need to understand specifically why the procedures are in place and how to follow them correctly. Having a competent person working on site means that you always have the resource you need to make good decisions. There also needs to be some recourse for employees who choose to work unsafely.
Photo used with permission from Benjamin Yaney.

## Slide 80: Competent Person
  one who is capable of identifying existing and predictable hazards in the surroundings…and who has authorization to take prompt corrective measures to eliminate them.
Notes: Competent Person-This definition is from OSHA. OSHA also says that a competent person can identify “working conditions which are unsanitary, hazardous, or dangerous to employees.” The employer is responsible to have and designate the competent person.

## Slide 81: Competent Person
Role & responsibilities:
Design structural ramps used for workers only
Monitor water removal operations
Inspection prior to work and during shift
Remove workers exposed to hazardous area
Take precautions for worker safety
Notes: Role-A competent person is designated by the employer and must be capable of 4 broad actions and have 1 broad authorization.
1-identify existing hazards
2-identify predictable hazards
3-identify hazardous working condition
-and be authorized to correct them all. Every trench or excavation site needs to have a competent person put their eyes on it at least once to perform their responsibilities.
Responsibilities-A competent person must inspect the site and protective systems daily for evidence of anything that could possibly cause a cave-in, failure of protective systems, hazardous atmosphere or another hazard. When hazards are found, they need to remove workers from them and take appropriate precautions before workers continue work. When water is being removed, they must specifically monitor water removal operations and equipment. They are also the one to design all structural ramps (steel or wood construction) for worker access only. If vehicles will use the ramp, a competent person in structural design must design the ramps.

## Slide 82: Competent Person
Role & responsibilities:
Examine ground of <5 ft. excavations
Examine damaged equipment used in protective systems
Classify and reclassify soil & rock
Reduce maximum slope based on surcharge loads
Evaluate the effects of surcharge
Notes: Responsibilities-A competent person can determine that an excavation less than 5 ft. in depth does not need a protective system after examining the ground. They are also expected to determine if damaged components of shoring or shielding are suitable for use or not. Another duty they have is to reduce the maximum slope in a sloping protective system if there are additional loads placed on the soil from equipment and other nearby structures. A final major responsibility of theirs is to classify soil and rock deposits and reclassify them if conditions affecting their classification change in any way.

## Slide 83: Designating the Competent Person
Who should it be within your crew?
Notes: The instructor should facilitate a discussion with the class.

## Slide 84: 1926.651
Surface encumbrances removed, supported
Utilities located, safely dug, supported, protected
Ramp design, no movement, uniform thickness
Notes: Surface encumbrances- All surface encumbrances that are located so as to create a hazard to employees shall be removed or supported, as necessary, to safeguard employees.
Underground installations- The estimated location of utility installations, such as sewer, telephone, fuel, electric, water lines, or any other underground installations that reasonably may be expected to be encountered during excavation work, shall be determined prior to opening an excavation.
Utility companies or owners shall be contacted within established or customary local response times, advised of the proposed work, and asked to establish the location of the utility underground installations prior to the start of actual excavation. When utility companies or owners cannot respond to a request to locate underground utility installations within 24 hours (unless a longer period is required by state or local law), or cannot establish the exact location of these installations, the employer may proceed, provided the employer does so with caution, and provided detection equipment or other acceptable means to locate utility installations are used.
When excavation operations approach the estimated location of underground installations, the exact location of the installations shall be determined by safe and acceptable means.
While the excavation is open, underground installations shall be protected, supported or removed as necessary to safeguard employees.
Access and egress -
Structural ramps that are used solely by employees as a means of access or egress from excavations shall be designed by a competent person. Structural ramps used for access or egress of equipment shall be designed by a competent person qualified in structural design, and shall be constructed in accordance with the design.
Ramps and runways constructed of two or more structural members shall have the structural members connected together to prevent displacement.
Structural members used for ramps and runways shall be of uniform thickness.
Cleats or other appropriate means used to connect runway structural members shall be attached to the bottom of the runway or shall be attached in a manner to prevent tripping.
Structural ramps used in lieu of steps shall be provided with cleats or other surface treatments on the top surface to prevent slipping.
Photo used with permission from Benjamin Yaney.

## Slide 85: 1926.651
Egress every 25 ft, high viz, falling loads, warning system
Atmospheres’ tested, controlled, retested
Rescue equipment available and attended, lifeline
Notes: Means of egress from trench excavations. A stairway, ladder, ramp or other safe means of egress shall be located in trench excavations that are 4 feet (1.22 m) or more in depth so as to require no more than 25 feet (7.62 m) of lateral travel for employees.
Exposure to vehicular traffic. Employees exposed to public vehicular traffic shall be provided with, and shall wear, warning vests or other suitable garments marked with or made of reflectorized or high-visibility material.
Exposure to falling loads. No employee shall be permitted underneath loads handled by lifting or digging equipment. Employees shall be required to stand away from any vehicle being loaded or unloaded to avoid being struck by any spillage or falling materials. Operators may remain in the cabs of vehicles being loaded or unloaded when the vehicles are equipped, in accordance with §1926.601(b)(6), to provide adequate protection for the operator during loading and unloading operations.
Warning system for mobile equipment. When mobile equipment is operated adjacent to an excavation, or when such equipment is required to approach the edge of an excavation, and the operator does not have a clear and direct view of the edge of the excavation, a warning system shall be utilized such as barricades, hand or mechanical signals, or stop logs. If possible, the grade should be away from the excavation.
Hazardous atmospheres -
Testing and controls. In addition to the requirements set forth in subparts D and E of this part (29 CFR 1926.50 - 1926.107) to prevent exposure to harmful levels of atmospheric contaminants and to assure acceptable atmospheric conditions, the following requirements shall apply:
Where oxygen deficiency (atmospheres containing less than 19.5 percent oxygen) or a hazardous atmosphere exists or could reasonably be expected to exist, such as in excavations in landfill areas or excavations in areas where hazardous substances are stored nearby, the atmospheres in the excavation shall be tested before employees enter excavations greater than 4 feet (1.22 m) in depth.
Adequate precautions shall be taken to prevent employee exposure to atmospheres containing less than 19.5 percent oxygen and other hazardous atmospheres. These precautions include providing proper respiratory protection or ventilation in accordance with subparts D and E of this part respectively.
Adequate precaution shall be taken such as providing ventilation, to prevent employee exposure to an atmosphere containing a concentration of a flammable gas in excess of 20 percent of the lower flammable limit of the gas.
When controls are used that are intended to reduce the level of atmospheric contaminants to acceptable levels, testing shall be conducted as often as necessary to ensure that the atmosphere remains safe.
Emergency rescue equipment.
Emergency rescue equipment, such as breathing apparatus, a safety harness and line, or a basket stretcher, shall be readily available where hazardous atmospheric conditions exist or may reasonably be expected to develop during work in an excavation. This equipment shall be attended when in use.
Employees entering bell-bottom pier holes, or other similar deep and confined footing excavations, shall wear a harness with a life-line securely attached to it. The lifeline shall be separate from any line used to handle materials, and shall be individually attended at all times while the employee wearing the lifeline is in the excavation.
Photo used with permission from Benjamin Yaney.

## Slide 86: 1926.651
Water accumulating precautions, monitoring, inspections
Existing structures supported or dig approved by PE
Protection from loose soil
Competent person inspections
Notes: Protection from hazards associated with water accumulation.
Employees shall not work in excavations in which there is accumulated water, or in excavations in which water is accumulating, unless adequate precautions have been taken to protect employees against the hazards posed by water accumulation. The precautions necessary to protect employees adequately vary with each situation, but could include special support or shield systems to protect from cave-ins, water removal to control the level of accumulating water, or use of a safety harness and lifeline.
If water is controlled or prevented from accumulating by the use of water removal equipment, the water removal equipment and operations shall be monitored by a competent person to ensure proper operation.
If excavation work interrupts the natural drainage of surface water (such as streams), diversion ditches, dikes, or other suitable means shall be used to prevent surface water from entering the excavation and to provide adequate drainage of the area adjacent to the excavation. Excavations subject to runoff from heavy rains will require an inspection by a competent person and compliance with paragraphs (h)(1) and (h)(2) of this section.
Stability of adjacent structures.
Where the stability of adjoining buildings, walls, or other structures is endangered by excavation operations, support systems such as shoring, bracing, or underpinning shall be provided to ensure the stability of such structures for the protection of employees.
Excavation below the level of the base or footing of any foundation or retaining wall that could be reasonably expected to pose a hazard to employees shall not be permitted except when:
A support system, such as underpinning, is provided to ensure the safety of employees and the stability of the structure; or
The excavation is in stable rock; or
A registered professional engineer has approved the determination that the structure is sufficently removed from the excavation so as to be unaffected by the excavation activity; or
A registered professional engineer has approved the determination that such excavation work will not pose a hazard to employees.
Sidewalks, pavements, and appurtenant structure shall not be undermined unless a support system or another method of protection is provided to protect employees from the possible collapse of such structures.
Protection of employees from loose rock or soil.
Adequate protection shall be provided to protect employees from loose rock or soil that could pose a hazard by falling or rolling from an excavation face. Such protection shall consist of scaling to remove loose material; installation of protective barricades at intervals as necessary on the face to stop and contain falling material; or other means that provide equivalent protection.
Employees shall be protected from excavated or other materials or equipment that could pose a hazard by falling or rolling into excavations. Protection shall be provided by placing and keeping such materials or equipment at least 2 feet (.61 m) from the edge of excavations, or by the use of retaining devices that are sufficient to prevent materials or equipment from falling or rolling into excavations, or by a combination of both if necessary.
Inspections.
Daily inspections of excavations, the adjacent areas, and protective systems shall be made by a competent person for evidence of a situation that could result in possible cave-ins, indications of failure of protective systems, hazardous atmospheres, or other hazardous conditions. An inspection shall be conducted by the competent person prior to the start of work and as needed throughout the shift. Inspections shall also be made after every rainstorm or other hazard increasing occurrence. These inspections are only required when employee exposure can be reasonably anticipated.
Where the competent person finds evidence of a situation that could result in a possible cave-in, indications of failure of protective systems, hazardous atmospheres, or other hazardous conditions, exposed employees shall be removed from the hazardous area until the necessary precautions have been taken to ensure their safety.
Walkways shall be provided where employees or equipment are required or permitted to cross over excavations. Guardrails which comply with §1926.502(b) shall be provided where walkways are 6 feet (1.8 m) or more above lower levels.
Photo used with permission from Benjamin Yaney.

## Slide 87: 1926.652
Cave-in protection requirements
Sloping and benching design
Support, shield and protective system design
Notes: Protection of employees in excavations.
Each employee in an excavation shall be protected from cave-ins by an adequate protective system designed in accordance with paragraph (b) or (c) of this section except when:
Excavations are made entirely in stable rock; or
Excavations are less than 5 feet (1.52m) in depth and examination of the ground by a competent person provides no indication of a potential cave-in.
Protective systems shall have the capacity to resist without failure all loads that are intended or could reasonably be expected to be applied or transmitted to the system.
Design of sloping and benching systems. The slopes and configurations of sloping and benching systems shall be selected and constructed by the employer or his designee and shall be in accordance with the requirements of paragraph (b)(1); or, in the alternative, paragraph (b)(2); or, in the alternative, paragraph (b)(3), or, in the alternative, paragraph (b)(4), as follows:
Option (1)-Allowable configurations and slopes
Excavations shall be sloped at an angle not steeper than one and one-half horizontal to one vertical (34 degrees measured from the horizontal), unless the employer uses one of the other options listed below.
Slopes specified in paragraph (b)(1)(i) of this section, shall be excavated to form configurations that are in accordance with the slopes shown for Type C soil in appendix B to this subpart.
Option (2)-Determination of slopes and configurations using Appendices A and B. Maximum allowable slopes, and allowable configurations for sloping and benching systems, shall be determined in accordance with the conditions and requirements set forth in appendices A and B to this subpart.
Option (3)-Designs using other tabulated data.
Designs of sloping or benching systems shall be selected from and be in accordance with tabulated data, such as tables and charts.
The tabulated data shall be in written form and shall include all of the following:
Identification of the parameters that affect the selection of a sloping or benching system drawn from such data;
Identification of the limits of use of the data, to include the magnitude and configuration of slopes determined to be safe;
Explanatory information as may be necessary to aid the user in making a correct selection of a protective system from the data.
At least one copy of the tabulated data which identifies the registered professional engineer who approved the data, shall be maintained at the jobsite during construction of the protective system. After that time the data may be stored off the jobsite, but a copy of the data shall be made available to the Secretary upon request.
Option (4)-Design by a registered professional engineer.
Sloping and benching systems not utilizing Option (1) or Option (2) or Option (3) under paragraph (b) of this section shall be approved by a registered professional engineer.
Designs shall be in written form and shall include at least the following:
The magnitude of the slopes that were determined to be safe for the particular project;
The configurations that were determined to be safe for the particular project; and
The identity of the registered professional engineer approving the design.
At least one copy of the design shall be maintained at the jobsite while the slope is being constructed. After that time the design need not be at the jobsite, but a copy shall be made available to the Secretary upon request.
Design of support systems, shield systems, and other protective systems. Designs of support systems shield systems, and other protective systems shall be selected and constructed by the employer or his designee and shall be in accordance with the requirements of paragraph (c)(1); or, in the alternative, paragraph (c)(2); or, in the alternative, paragraph (c)(3); or, in the alternative, paragraph (c)(4) as follows:
Option (1)-Designs using appendices A, C and D. Designs for timber shoring in trenches shall be determined in accordance with the conditions and requirements set forth in appendices A and C to this subpart. Designs for aluminum hydraulic shoring shall be in accordance with paragraph (c)(2) of this section, but if manufacturer's tabulated data cannot be utilized, designs shall be in accordance with appendix D.
Option (2)-Designs Using Manufacturer's Tabulated Data.
Design of support systems, shield systems, or other protective systems that are drawn from manufacturer's tabulated data shall be in accordance with all specifications, recommendations, and limitations issued or made by the manufacturer.
Deviation from the specifications, recommendations, and limitations issued or made by the manufacturer shall only be allowed after the manufacturer issues specific written approval.
Manufacturer's specifications, recommendations, and limitations, and manufacturer's approval to deviate from the specifications, recommendations, and limitations shall be in written form at the jobsite during construction of the protective system. After that time this data may be stored off the jobsite, but a copy shall be made available to the Secretary upon request.
Option (3)-Designs using other tabulated data.
Designs of support systems, shield systems, or other protective systems shall be selected from and be in accordance with tabulated data, such as tables and charts.
The tabulated data shall be in written form and include all of the following:
Identification of the parameters that affect the selection of a protective system drawn from such data;
Identification of the limits of use of the data;
Explanatory information as may be necessary to aid the user in making a correct selection of a protective system from the data.
At least one copy of the tabulated data, which identifies the registered professional engineer who approved the data, shall be maintained at the jobsite during construction of the protective system. After that time the data may be stored off the jobsite, but a copy of the data shall be made available to the Secretary upon request.
Option (4)-Design by a registered professional engineer.
Support systems, shield systems, and other protective systems not utilizing Option 1, Option 2 or Option 3, above, shall be approved by a registered professional engineer.
Designs shall be in written form and shall include the following:
A plan indicating the sizes, types, and configurations of the materials to be used in the protective system; and
The identity of the registered professional engineer approving the design.
At least one copy of the design shall be maintained at the jobsite during construction of the protective system. After that time, the design may be stored off the jobsite, but a copy of the design shall be made available to the Secretary upon request.
Photo used with permission from Benjamin Yaney.

## Slide 88: 1926.652
Materials & equipment condition
Installation & removal of support-bottom up
Installation & excavation coordinated
Notes: Materials and equipment.
Materials and equipment used for protective systems shall be free from damage or defects that might impair their proper function.
Manufactured materials and equipment used for protective systems shall be used and maintained in a manner that is consistent with the recommendations of the manufacturer, and in a manner that will prevent employee exposure to hazards.
When material or equipment that is used for protective systems is damaged, a competent person shall examine the material or equipment and evaluate its suitability for continued use. If the competent person cannot assure the material or equipment is able to support the intended loads or is otherwise suitable for safe use, then such material or equipment shall be removed from service, and shall be evaluated and approved by a registered professional engineer before being returned to service.
Installation and removal of support-
Members of support systems shall be securely connected together to prevent sliding, falling, kickouts, or other predictable failure.
Support systems shall be installed and removed in a manner that protects employees from cave-ins, structural collapses, or from being struck by members of the support system.
Individual members of support systems shall not be subjected to loads exceeding those which those members were designed to withstand.
Before temporary removal of individual members begins, additional precautions shall be taken to ensure the safety of employees, such as installing other structural members to carry the loads imposed on the support system.
Removal shall begin at, and progress from, the bottom of the excavation. Members shall be released slowly so as to note any indication of possible failure of the remaining members of the structure or possible cave-in of the sides of the excavation.
Backfilling shall progress together with the removal of support systems from excavations.
Additional requirements for support systems for trench excavations.
Excavation of material to a level no greater than 2 feet (.61 m) below the bottom of the members of a support system shall be permitted, but only if the system is designed to resist the forces calculated for the full depth of the trench, and there are no indications while the trench is open of a possible loss of soil from behind or below the bottom of the support system.
Installation of a support system shall be closely coordinated with the excavation of trenches.
Photo used with permission from Benjamin Yaney.

## Slide 89: 1926.652
Working above employees on slope or bench
Shield installation and removal
Sudden lateral loads on shield
Notes: Sloping and benching systems. Employees shall not be permitted to work on the faces of sloped or benched excavations at levels above other employees except when employees at the lower levels are adequately protected from the hazard of falling, rolling, or sliding material or equipment.
Shield systems-
Shield systems shall not be subjected to loads exceeding those which the system was designed to withstand.
Shields shall be installed in a manner to restrict lateral or other hazardous movement of the shield in the event of the application of sudden lateral loads.
Employees shall be protected from the hazard of cave-ins when entering or exiting the areas protected by shields.
Employees shall not be allowed in shields when shields are being installed, removed, or moved vertically.
Additional requirement for shield systems used in trench excavations. Excavations of earth material to a level not greater than 2 feet (.61 m) below the bottom of a shield shall be permitted, but only if the shield is designed to resist the forces calculated for the full depth of the trench, and there are no indications while the trench is open of a possible loss of soil from behind or below the bottom of the shield.
Photo used with permission from Benjamin Yaney.

## Slide 90: Appendix A
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Soil classification
Visual tests
Manual tests
Notes: Appendix A details out the 4 soil classifications that OSHA recognizes and methods to classify them.
Image credit-creative commons.

## Slide 91: Soil Classification
USDA Soil Texture Calculator (link)
Classifications:
Stable rock
Type A
Type B
Type C
Notes: OSHA classifications-OSHA classifies soil as one of the following:
-Stable rock
-Type A (cohesive with unconfined compressive strength > 1.5 tons/sq. ft.). Examples include clay, silty clay, sandy clay and clay loam.
-Type B (cohesive with unconfined compressive strength between 0.5 and 1.5 tons/sq. ft.). Examples include silt, silt loam, sandy clay loam, silty clay loam and angular gravel.
-Type C (cohesive with unconfined compressive strength less than 0.5 tons/sq. ft.). Examples include gravel, sand, loamy sand or sandy loam and soil with freely seeping water.
OSHA requires at least one visual test and one manual test be performed by the competent person before classifying soil. It is a good idea to document the soil classification each time it is made, including what tests were used and the results of each.
The chart shown depicts soil classifications with percent sand, silt and clay along the three sides.
Image credit-creative commons.

## Slide 92: Definition
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Stable Rock:
  natural solid mineral material that can be excavated with vertical sides and will remain intact while exposed.
Notes: Stable rock-This definition is from OSHA. OSHA also says, “unstable rock is considered to be stable when the rock material on the side or sides of the excavation is secured against caving-in or movement by rock bolts or by another protective system that has been designed by a registered professional engineer.”
Photo credit-creative commons.

## Slide 93: Type A Soil
Cohesive with unconfined compressive strength > 1.5 tons/sq. ft.
Undisturbed
Stable
Cohesive = Clay
  Silty Clay
  Sandy Clay
  Clay Loam
  Silty Clay Loam
  Sandy Clay Loam
Notes: Type A soil is cohesive and has a high unconfined compressive strength; 1.5 tons per square foot or greater. Examples of type A soil include clay, silty clay, sandy clay, and clay loam.

## Slide 94: Type A Soil (cont.)
Uncommon
No Soil is Type A if:
  Soil has been previously disturbed
  Soil is fissured
  Soil is subject to vibration from heavy traffic, pile driving, or similar effects
Notes: Soil cannot be classified as type A if it is fissured, if it has been previously disturbed, if it has water seeping through it, or if it is subject to vibration from sources such as heavy traffic or pile drivers.

## Slide 95: Type B Soil
Previously disturbed
Granular cohesionless soils (crushed rock)
Soil that meets the unconfined compressive strength or cementation requirements for Type A, but is fissured or subject to vibration; or
Dry rock that is not stable; or
Material that is part of a sloped, layered system where the layers dip into the excavation on a slope less steep than four horizontal to one vertical (4H:1V), but only if the material would otherwise be classified as Type B.
Cohesive with unconfined compressive strength between 0.5 and 1.5 tons/sq.ft.
Notes: Type B soil is cohesive and has often been cracked or disturbed, with pieces that don't stick together as well as Type A soil. Type B soil has medium unconfined compressive strength; between 0.5 and 1.5 tons per square foot. Examples of Type B soil include angular gravel, silt, silt loam, and soils that are fissured or near sources of vibration, but could otherwise be Type A.

## Slide 96: Type C Soil
Cohesive with unconfined compressive strength less than 0.5 tons/sq. ft.
Granular
Gravel
Sand
Submerged soil or soil from which water is freely seeping
Notes: Type C soil is the least stable type of soil. Type C includes granular soils in which particles don't stick together and cohesive soils with a low unconfined compressive strength; 0.5 tons per square foot or less. Examples of Type C soil include gravel, and sand. Because it is not stable, soil with water seeping through it is also automatically classified as Type C soil, regardless of its other characteristics.

## Slide 97: Soil Testing
Visual tests:
Grain
Clumps vs. breaks easily
Fissured material
Previously disturbed
Layers
Water
Vibration
Notes: Visual tests. Visual analysis is conducted to determine qualitative information regarding the excavation site in general, the soil adjacent to the excavation, the soil forming the sides of the open excavation, and the soil taken as samples from excavated material.
(i) Observe samples of soil that are excavated and soil in the sides of the excavation. Estimate the range of particle sizes and the relative amounts of the particle sizes. Soil that is primarily composed of fine-grained material is cohesive material. Soil composed primarily of coarse-grained sand or gravel is granular material.
(ii) Observe soil as it is excavated. Soil that remains in clumps when excavated is cohesive. Soil that breaks up easily and does not stay in clumps is granular.
(iii) Observe the side of the opened excavation and the surface area adjacent to the excavation. Crack-like openings such as tension cracks could indicate fissured material. If chunks of soil spall off a vertical side, the soil could be fissured. Small spalls are evidence of moving ground and are indications of potentially hazardous situations.
(iv) Observe the area adjacent to the excavation and the excavation itself for evidence of existing utility and other underground structures, and to identify previously disturbed soil.
(v) Observed the opened side of the excavation to identify layered systems. Examine layered systems to identify if the layers slope toward the excavation. Estimate the degree of slope of the layers.
(vi) Observe the area adjacent to the excavation and the sides of the opened excavation for evidence of surface water, water seeping from the sides of the excavation, or the location of the level of the water table.
(vii) Observe the area adjacent to the excavation and the area within the excavation for sources of vibration that may affect the stability of the excavation face.
Photo-this photo shows that existing underground utilities were uncovered, so the soil must have been previously disturbed when they were put in.
Photo used with permission from Benjamin Yaney.

## Slide 98: Soil Testing
This image courtesy of creative commons.
Manual tests:
Plasticity
Dry strength
Thumb penetration
Other strength tests
Drying
Notes: Manual tests. Manual analysis of soil samples is conducted to determine quantitative as well as qualitative properties of soil and to provide more information in order to classify soil properly.
(i) Plasticity. Mold a moist or wet sample of soil into a ball and attempt to roll it into threads as thin as 1/8-inch in diameter. Cohesive material can be successfully rolled into threads without crumbling. For example, if at least a two-inch (50 mm) length of 1/8-inch thread can be held on one end without tearing, the soil is cohesive.
(ii) Dry strength. If the soil is dry and crumbles on its own or with moderate pressure into individual grains or fine powder, it is granular (any combination of gravel, sand, or silt). If the soil is dry and falls into clumps which break up into smaller clumps, but the smaller clumps can only be broken up with difficulty, it may be clay in any combination with gravel, sand or silt. If the dry soil breaks into clumps which do not break up into small clumps and which can only be broken with difficulty, and there is no visual indication the soil is fissured, the soil may be considered unfissured.
(iii) Thumb penetration. The thumb penetration test can be used to estimate the unconfined compressive strength of cohesive soils. (This test is based on the thumb penetration test described in American Society for Testing and Materials (ASTM) Standard designation D2488 - "Standard Recommended Practice for Description of Soils (Visual - Manual Procedure).") Type A soils with an unconfined compressive strength of 1.5 tsf can be readily indented by the thumb; however, they can be penetrated by the thumb only with very great effort. Type C soils with an unconfined compressive strength of 0.5 tsf can be easily penetrated several inches by the thumb and can be molded by light finger pressure. This test should be conducted on an undisturbed soil sample, such as a large clump of spoil, as soon as practicable after excavation to keep to a minimum the effects of exposure to drying influences. If the excavation is later exposed to wetting influences (rain, flooding), the classification of the soil must be changed accordingly.
(iv) Other strength tests. Estimates of unconfined compressive strength of soils can also be obtained by use of a pocket penetrometer or by using a hand-operated shearvane.
(v) Drying test. The basic purpose of the drying test is to differentiate between cohesive material with fissures, unfissured cohesive material, and granular material. The procedure for the drying test involves drying a sample of soil that is approximately one inch thick (2.54 cm) and six inches (15.24 cm) in diameter until it is thoroughly dry:
(A) If the sample develops cracks as it dries, significant fissures are indicated.
(B) Samples that dry without cracking are to be broken by hand. If considerable force is necessary to break a sample, the soil has significant cohesive material content. The soil can be classified as an unfissured cohesive material and the unconfined compressive strength should be determined.
(C) If a sample breaks easily by hand, it is either a fissured cohesive material or a granular material. To distinguish between the two, pulverize the dried clumps of the sample by hand or by stepping on them. If the clumps do not pulverize easily, the material is cohesive with fissures. If they pulverize easily into very small fragments, the material is granular.
Image credit-creative commons.

## Slide 99: Appendix B
C
B
A
Stable rock
Max allowable slope
  Stable Rock (90⁰)
  Type A soil (53⁰)
  Type B soil (45⁰)
  Type C soil (34⁰)
  Layered (each layer separate)
Notes: Appendix B cover the maximum allowable slope for sloping and benching operations based on soil type. The general allowances are shown in the diagram.
Additional details in this appendix include max slopes for layered excavations, short term allowances and for when shoring or shielding is in the lower part of the excavation. Supports and shields are to extend 18 inches above the vertical side.

## Slide 100: Appendix C
Table C 1.1
Timber Trench Shoring– Minimum Timber Requirements*
Soil Type A
Table C 1.2
Timber Trench Shoring– Minimum Timber Requirements*
Soil Type B
Table C 1.3
Timber Trench Shoring– Minimum Timber Requirements*
Soil Type C
Timber shoring tables
Limitations
Notes: Appendix C details timber shoring requirements in table form for each type of soil. The table headers are shown on this slide.
Image credit-OSHA.
https://www.osha.gov/laws-regs/regulations/standardnumber/1926/1926SubpartPAppC

## Slide 101: Appendix C
Timber shoring tables
One for each soil type
Specify
  Cross brace spacing
  Wales size & spacing
  Upright spacing

## Slide 102: Appendix C
Limitations:
Loads near trench exceed 2ft. soil surcharge
Vertical loads on cross braces exceed 240lb./ sq. ft.
Surcharge from equipment over 20,000lb.
Only the lower part of trench is shored

## Slide 103: Appendix D
Table D 1.1
Aluminum Hydraulic Shoring
Vertical Shores for Soil Type A
Table D 1.2
Aluminum Hydraulic Shoring
Vertical Shores for Soil Type b
Table D 1.3
Aluminum Hydraulic Shoring
Vertical Shores for Soil Type c
Hydraulic aluminum shoring tables
Limitations
Notes: Appendix D details aluminum hydraulic shoring requirements in table form for each type of soil. The table headers are shown on this slide.
Image credit-OSHA.
https://www.osha.gov/laws-regs/regulations/standardnumber/1926/1926SubpartPAppD

## Slide 104: Appendix D
Hydraulic aluminum shoring tables
One for each soil type
Specify
  Cylinder diameters
  Maximum horizontal spacing
  Maximum vertical spacing

## Slide 105: Appendix D
Limitations:
Vertical loads on cross brace exceed 100lb./sq. ft.
Surcharge from equipment over 20,000lb.
Only the lower part of trench is shored

## Slide 106: Appendix E
These images courtesy of OSHA.
Alternatives to timber shoring
Notes: Appendix E depicts four alternatives to timber shoring-aluminum hydraulic, pneumatic/hydraulic, trench jacks and trench shields. Each come with their pros and cons, but they are generally more predictable and easier to install than timber shoring. This is due to the simpler regulations to follow and materials used.
Image credit-OSHA.
https://www.osha.gov/laws-regs/regulations/standardnumber/1926/1926SubpartPAppE

## Slide 107: Appendix F
Decision trees for selection of protective systems:
1-are protective systems needed?
2-what standard to follow for sloping?
3-what standard to follow for shoring & shielding?
Notes: Appendix F displays three decision trees. The first on if protective systems are needed and then which tree to go to next. The next concerns what regulation to follow for sloping. It will either be

## Slide 108: Appendix F
Go to Fig. 3
Shoring or Shielding Selected
Go to Fig. 2
Sloping Selected
YES
Excavation may be made with vertical sides.
YES
NO
Excavation must be sloped, shored or shielded.
NO
Is the excavation entirely in stable rock?
YES
NO
Is there potential for cave-in?
Excavation more than 5 feet in depth
Notes: Adapted from OSHA https://www.osha.gov/laws-regs/regulations/standardnumber/1926/1926SubpartPAppF

## Slide 109: Appendix F
Excavations must comply with 1926.652 (b)(1) which requires a slope of 1.5H:1V (34 degrees)
Excavations must comply with one of the following options:
1926.652 (b)(2) App. A and B to be followed.
1926.652 (b)(3) other tabulated data to be followed
1926.652 (b)(4) excavation is designed by a registered professional engineer.
NO
YES
Will soil classification be made in accordance with 1926.652 (b)?
Sloping selected as the method of protection
Figure 2
Notes: Adapted from OSHA https://www.osha.gov/laws-regs/regulations/standardnumber/1926/1926SubpartPAppF

## Slide 110: Appendix F
1926.652 (c)(1) requires App. A and C to be followed (Timber Shoring)
1926.652 (c)(2) requires manufacturers data to be followed (Hydraulic Shoring, Trench Jacks, Air Shores, Shield)
1926.652 (c)(3) requires tabulated data (see definition) to be followed (any system as per tabulated data)
1926.652 (c)(4) requires excavation to be designed by a registered professional engineer (any designed system)
Soil Classification Required
Excavation must comply with 1 of the 4 options
Shoring or shielding selected as the method of protection
Figure 3
Notes: Adapted from OSHA https://www.osha.gov/laws-regs/regulations/standardnumber/1926/1926SubpartPAppF

## Slide 111: Recommended Practices for Safety and Health Programs
Notes: Safety and health programs foster a proactive approach to “finding and fixing” workplace hazards before they can cause injury or illness. Rather than reacting to an incident, management and workers collaborate to identify and solve issues before they occur. This collaboration builds trust, enhances communication, and often leads to other business improvements.

## Slide 112: OSHA’s Safety and Health System Model
TRAINING
HAZARD PREVENTION & CONTROL
WORKSITE ANALYSIS
MANAGEMENT LEADERSHIP & EMPLOYEE INVOLVEMENT

## Slide 113: Management Leadership
Management provides the leadership, vision, and resources needed to implement an effective safety and health program.
There must be a commitment from the top to implementing a program
When sincere and supported by actions, workers know that safety and health are important/valued.
Notes: Management Leadership
Management leadership means there is a commitment from the top to implementing a program and using it to drive continuous improvement in safety and health.
Why Is It Important?
When management leadership is sincere and is supported by actions, workers know that safety and health are important to business success. This means that the steps they take to improve safety and health will be valued by the business.
Top management can demonstrate its commitment in many different ways, including:
Developing and communicating a safety and health policy statement.
Providing the resources needed to implement and operate the program.
Factoring safety and health into operational planning and decisions.
Recognizing or rewarding safety and health contributions and achievements.
Leading by example, by practicing safe behaviors and making safety part of daily conversations.

## Slide 114: Management Leadership
Business owners, managers, and supervisors:
    Make worker safety and health a core organizational value
    Are fully committed to eliminating hazards, protecting workers, and continuously improving workplace safety and health
    Provide sufficient resources
    Visibly demonstrate and communicate their safety and health commitment to workers and others
    Set an example through their own actions
Notes: Management provides the leadership, vision, and resources needed to implement an effective safety and health program. Management leadership means that business owners, managers, and supervisors:
• Make worker safety and health a core organizational value.
• Are fully committed to eliminating hazards, protecting workers, and continuously improving workplace safety and health.
• Provide sufficient resources to implement and maintain the safety and health program.
• Visibly demonstrate and communicate their safety and health commitment to workers and others.
• Set an example through their own actions.
Top management can demonstrate its commitment in many different ways, including:
  Developing and communicating a safety and health policy statement.
  Providing the resources needed to implement and operate the program.
  Factoring safety and health into operational planning and decisions.
  Recognizing or rewarding safety and health contributions and achievements.
  Leading by example, by practicing safe behaviors and making safety part of daily conversations.

## Slide 115: Why Should Employees be Involved?
Workers know potential hazards and have a vested interest in effective protection.
Group input provides a wider range of experience.
Employees are more likely to support and use programs in which they have input.

## Slide 116: Job Hazard Analysis (JHA)
COMPANY/ PROJECT NAME or ID/ LOCATION ( City, State) |  | DATE | NEW REVISED |  |  | PAGE 1 of 3
WORK ACTIVITY (Description): Excavation & Trenching |  |  |  |  |  | 
DEVELOPMENT TEAM | POSITION / TITLE | REVIEWED BY: |  | POSITION / TITLE |  | 
 | Safety Manager |  |  | Sr. Project Manager |  | 
 | Site Manager |  |  |  |  | 
 | Project Engineer |  |  |  |  | 
MINIMUM REQUIRED PERSONAL PROTECTIVE EQUIPMENT ( SEE CRITICAL ACTIONS FOR TASK-SPECIFIC REQUIREMENTS) |  |  |  |  |  | 
REFLECTIVE VEST HARD HAT LIFELINE / HARNESS SAFETY GLASSES | GOGGLES FACE SHIELD HEARING PROTECTION SAFETY SHOES | AIR PURIFYING RESPIRATOR SUPPLIED RESPIRATOR PPE CLOTHING |  |  | GLOVES Cut-resistant OTHER Chaps | 
¹JOB STEPS | ²POTENTIAL HAZARDS | ³CRITICAL ACTIONS TO MITIGATE HAZARDS |  |  |  | 
underground drawings and excavation permit | Underground utilities, footings, or foundations are not identified they may be damaged during excavation, causing property damage, personal injury, or accidentally shutting down vital plant processes causing potential shut down of unit or units | Call 811 for utility checks and marking (811 will not locate local water lines) Attains and understands drawings identifying underground structures in the excavation location including sewers, oily water and storm water, firewater, service water, potable water, electrical, product lines, and/or natural gas mains, pipelines, etc., foundations and footings and share this information with all employees on job during pre-job planning and toolbox meetings, to ensure excavations will not damage under-ground utilities or lines or affect the stability of any surrounding buildings, vessels, or structures |  |  |  | 
Sections:
Job steps
Potential hazards
Critical actions to mitigate hazards
Minimum required PPE
Notes: Hazard identification & assessment-hazards will exist in every workplace, the and the first step is finding them. Hazards are best identified when you get more eyes looking for them and then document what is found. Job Safety Analyses break jobs into steps and help ensure that a detailed level of observation is given to finding hazards with those jobs. A JSA for the excavation, installation of protective systems, work done in the excavation or trench, and closing the hole and clean up should be done at a minimum.
Inspections are required in many OSHA standards and they help with the process of making sure that we are checking the things we know to check. Things wear out and safety is compromise when they fail while in use. Protective systems need to be inspected for damage, the site need to be inspected each day for hazards and changes in conditions. Inspections help us stay on the preventative side.
Finally, once we have found hazards prioritizing them according to risk (severity and frequency of occurrence) is the next step. We almost always want to address the riskier problems first, because it is likely that we cannot fix everything at once and eliminate all hazards. Cave-ins and falls are the two biggest safety concerns for trench and excavation work.

## Slide 117: Inspections
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY
Inspect for:
Hazards
Access & egress
Confined spaces
PPE
Housekeeping
Notes: Hazard prevention & control-employers can really get into trouble when they know about hazards but do nothing to protect their employees from them. JSAs include preventative measures for each hazard found and are a great tool to keep on site. The supervisor, foremen or competent person should be ensuring that preventative measures on the JSAs are performed.
Daily safety talks with workers is also a good way to prevent and control hazards. Repetition is proven to help things stick in people’s minds, so with safety they are more likely to remember safe work practices and how to safely deal with hazards. There are multitudes of ready-to-go talks on cave-ins, trench safety, slips, trips, and falls. These would be good to do each week, and there should also be time for workers to voice concerns, ask questions and give suggestions.
Procedures are also a solid way to prevent and control hazards. There is nothing unclear about having workers follow established written procedures. Excavation and trench procedures should cover initial site evaluation, soil classification, reclassification, protective measures, inspections, and responsibilities.

## Slide 118: Inspections
This image courtesy of creative commons.
This Photo by Unknown Author is licensed under CC BY-SA
Inspect for:
Failure of protective systems
Accumulated water/soil moisture
Cracks, sloughing, bulging
Notes: Education & training-education is the impartation o f knowledge to someone while training is teaching them how to do something. Both parts need to be planned out and thought through to be effective and OSHA specifies a lot of training requirements. One key for both is to test the learner’s knowledge afterward to confirm that the education or training was successful.
A safety program should teach the value of safety. This is done from a compliance standpoint (it’s the law), a financial standpoint (cost of injuries, fatalities), and a moral and emotional standpoint (it is the right thing, and we care about people’s lives).
Education and training will sometimes need to be specific for the work being done. This would include working with soil, operating equipment, etc. Make sure that the people receiving it need to know it. As for general education and training-those are things everyone benefits from. An example here is how to recognize hazards or how to report incidents.

## Slide 119: Training
Connect with your audience;
  Who, what, and why?
Everyone should know their role
Make sure your training is:
  Immediately useful
  Relevant
Make sure your attitude is:
  Welcoming, Engaging, and Respectful
Notes: Developing useful training modules is key. Here are some helpful tips.

## Slide 120: Training
For Workers
Hazard recognition
Reporting procedure
Best practices
Notes: Workers will benefit from three basic training topics-hazard recognition, reporting procedures and best practices for the job they are doing. None of these topics require a full day of training, but there are losses when training is not provided at all. Workers need to understand trench and excavation hazards such as cave-ins and falls. They also need to know what to do when they notice something unsafe or an incident happens. It is always right to stop work and get the situation addressed before someone gets hurt. Finally, best practices help them perform the work the right way and not cut corners or miss steps.

## Slide 121: Training
For Managers
Decision making
Hazard correction
Standard requirements
Notes: Managers need training on how to make the right decisions. Again, worker safety needs to be such a value that a manager does not risk safety to meet a schedule or save money. Managers also have responsibility for correcting known hazards. Sometimes it might be as simple as instructing all workers to stay away from a hazard. Other times it might require a detailed plan and execution of it. Finally, management must be aware of applicable standard requirements. Fortunately, OSHA specifies a lot of items in Subpart P so that makes it easier to know how to proceed with a lot of work.

## Slide 122: Training
For Competent Person
Design structural ramps used for workers only
Monitor water removal operations
Inspection prior to work and during shift
Notes: The competent person has additional responsibilities under Subpart P and will need specific training on those. Role-A competent person is designated by the employer and must be capable of 4 broad actions and have 1 broad authorization.
1-identify existing hazards
2-identify predictable hazards
3-identify hazardous working condition
-and be authorized to correct them all. Every trench or excavation site needs to have a competent person put their eyes on it at least once to perform their responsibilities.
A competent person must inspect the site and protective systems daily for evidence of anything that could possibly cause a cave-in, failure of protective systems, hazardous atmosphere or another hazard. When water is being removed, they must specifically monitor water removal operations and equipment. They are also the one to design all structural ramps (steel or wood construction) for worker access only. If vehicles will use the ramp, a competent person in structural design must design the ramps.

## Slide 123: Training
For Competent Person
Remove workers exposed to hazardous area
Take precautions for worker safety
Examine ground of <5 ft. excavations
Notes: A competent person can determine that an excavation less than 5 ft. in depth does not need a protective system after examining the ground. When hazards are found, they need to remove workers from them and take appropriate precautions before workers continue work.

## Slide 124: Training
For Competent Person
Examine damaged equipment used in protective systems
Classify and reclassify soil & rock
Reduce maximum slope based on surcharge loads
Notes: They are also expected to determine if damaged components of shoring or shielding are suitable for use or not. Another duty they have is to reduce the maximum slope in a sloping protective system if there are additional loads placed on the soil from equipment and other nearby structures. A final major responsibility of theirs is to classify soil and rock deposits and reclassify them if conditions affecting their classification change in any way.

## Slide 125: Review
  Describe worker rights
  Describe employer responsibilities
  Define key terms
Notes: Spend a few minutes reviewing materials, ensuring the learning objectives are met.

## Slide 126: Review
  Review frequency of incidents
  Review costs of penalties
  Identify one hazard, cause and remedy
Notes: Spend a few minutes reviewing materials, ensuring the learning objectives are met.

## Slide 127: Review
  Name specific excavation requirement
  Name protective system requirement
  Name a few appendix topics
Notes: Spend a few minutes reviewing materials, ensuring the learning objectives are met.

## Slide 128: Review
  Name safety program element
  Name training element
  Describe responsibility of competent person
Notes: Spend a few minutes reviewing materials, ensuring the learning objectives are met.

## Slide 129: Let’s Test Our Knowledge
Post-class Quiz

## Slide 130: Post-Assessment (Q1)
Structural ramps used solely by employees as a means of access and egress from excavations shall be designed by a:
Qualified Engineer
Competent Person
Architect
Employees
Notes: The Answer is B

## Slide 131: Post-Assessment (Q2)
2. Excavations must be inspected daily by an Authorized Person.
True
False
Notes: The Answer is B

## Slide 132: Post-Assessment (Q3)
3. A “Trench Shield”, commonly known as a “Trench Box” in the field, is an engineered system designed to protect those who are working in a trench.
a. True
b. False
Notes: The Answer is A
This question may be confusing for students and the instructor should state that a “Trench Shield” is commonly known as, or commonly referred to as a “Trench Box” in the course.

## Slide 133: Post-Assessment (Q4)
4. A Trench and an Excavation is the same thing:
True
False
Notes: The Answer is B

## Slide 134: Post-Assessment (Q5)
5. Excavations greater than _____ ft. shall be tested before employees enter where potentially ______________ atmospheres could reasonably exist.
4’, Hazardous
4’, Ambient
6’, Hazardous
6’, Ambient
Notes: The Answer is A

## Slide 135: Post-Assessment (Q6)
6. The bottom of a trench shield (trench box) should be no more than ______ ft. above the bottom of the trench or excavation?
5’
3’
1’
2’
Notes: The Answer is D

## Slide 136: Post-Assessment (Q7)
7. ___________ cause/causes the most deaths in excavations.
Underground utilities
Water accumulation
Cave ins
Heavy equipment
Notes: The Answer is C

## Slide 137: Post-Assessment (Q8)
8. In excavations deeper than 4’ a means of exit _________.
Is not needed
Must be located within 100’ of workers
Must be located within 200’ of workers
Must be located within 25’ of workers
Notes: The Answer is D

## Slide 138: Post-Assessment (Q9)
9. Which of the following statements is not true about Type C soil:
If type is unknown, you should assume all soil is Type C
If sloped, it requires an angle of 34°
It can be benched
Type C soil is usually very loose and prone to cave in
Notes: The Answer is C

## Slide 139: Post-Assessment (Q10)
10. ______________ involves angling back the material in a continuous plane.
Shoring
Shielding
Sloping
Benching
Notes: The Answer is C

## Slide 140: References
Bureau of Labor Statistics-https://www.bls.gov/data/#injuries
Occupational Safety & Health Administration(OSHA), Trenching & Excavation Hazards & Solutions-https://www.osha.gov/SLTC/trenchingexcavation/solutions.html
OSHA, Fact Sheet-https://www.osha.gov/OshDoc/data_Hurricane_Facts/trench_excavation_fs.pdf
NIOSH Science Blog-https://blogs-origin.cdc.gov/niosh-science-blog/2019/06/06/trenching/
ELCOSH-http://elcosh.org/index.php
CPWR-https://www.cpwr.com/trench-safety
OSHA Regulations, 1926.650-https://www.osha.gov/laws-regs/regulations/standardnumber/1926
OSHA Recommended Practices for Safety and Health Programs https://www.osha.gov/shpguidelines/management-leadership.html
OSHA’s Safe + Sound webpage https://www.osha.gov/safeandsound/safety-and-health-programs.html